## Slide 1
Hardware-Aware Real-Time Low-Light Image Enhancement for Lane Detection
Praneel Vipul Vania (202201131)
Aditya Sable (202201049)
Under the guidance of:
Prof. Pankaj Kumar

## Slide 2
Problem Statement & Motivation
  Lane detection relies on clear visibility of road markings
  Low-light conditions reduce contrast and weaken edge information
  This leads to unstable or incorrect lane detection results
  Existing enhancement methods improve visibility but are often too slow for real-time use
  There is a need for an efficient real-time enhancement pipeline
Can we improve visibility while still maintaining real-time performance?

## Slide 3
Project Evolution Overview
Research Paper on low-light image enhancement
Identified Limitations
Proposed Improvements
Implementation
Integrated with Lane Detection

## Slide 4
Method
  Image converted from RGB to HSV color space
  Illumination estimated using Gaussian filtering on V channel
  Adaptive brightness enhancement applied
  Two enhanced outputs (V1 and V2) generated
  Wavelet fusion (max rule) used to combine results
Limitations
  Gaussian filtering causes edge blurring
  Over-enhancement in already bright regions
  Noise amplification in dark areas

## Slide 5
Proposed Improvements
  Replaced Gaussian filter with guided filter for better edge preservation
  Introduced darkness-based adaptive scaling to avoid over-enhancement
  Applied variance-based wavelet fusion for smoother and stable results
  Improved overall enhancement quality while maintaining structural details

## Slide 6
Explored Approaches
HSV-Based Enhancement
HSV → Gaussian Illumination → Adaptive Scaling → Output
Multi-Scale Illumination
HSV → Multi-Scale Gaussian → Adaptive Enhancement → Output
Gamma + CLAHE Pipeline
HSV → Gamma Correction → CLAHE → Denoising → Output
Retinex-Based Enhancement
HSV → Illumination Estimation → Retinex → CLAHE → Output
Fusion-Based Method (Paper)
HSV → Dual Outputs → Wavelet Fusion (Max Rule) → Output
Final Selected Pipeline
HSV → Guided Filter → Adaptive Scaling → Dual Outputs →
Wavelet → Variance Fusion → Output
All of the above approaches were tested on a dataset of 50 images

## Slide 7
Final Enhancement Pipeline

## Slide 8
  Significant improvement in low-light image visibility
  Better preservation of structural details and edges
  Enhanced contrast and clarity of road features
  Balanced brightness enhancement without over-saturation
Enhancement Results Statistics
Qualitative and Quantitative Improvements
  PSNR – measures overall image quality improvement
  SSIM – measures similarity preservation
  AMBE – measures brightness consistency
Evaluation Metrics Used

## Slide 9
ENHANCEMENT RESULTS
[Before → After]
[Before → After]

## Slide 10
Transition to Real-Time Processing
  Initial work focused on developing a high-quality enhancement pipeline
  Designed primarily for offline image processing
  During extension to lane detection and live video, computational limitations were observed
  Required redesign of the pipeline for real-time performance
From Offline Enhancement → Real-Time System

## Slide 11
Real-Time Enhancement Pipeline
Input
HSV Conversion
Smoothing (Bilateral Filter)
Adaptive Enhancement
Gaussian Illumination Estimation
Sharpening
Enhanced Frame Output
Enhanced Frame

## Slide 12
Lane Detection Pipeline

## Slide 13
Lane Detection Pipeline Result
Enhanced Input
Grayscale Conversion
Gaussian Blur
Canny Edge Detection
Region of Interest
Hough Transform
Lane Lines
Final Output

## Slide 14
Video Demonstration
Real-Time Lane Detection in Action

## Slide 15
Hardware Implementation (PYNQ-Z2)
  Deployed the pipeline on PYNQ-Z2 development board
  Used external camera for real-time input
  Processing performed on embedded ARM processor
  Achieved ~9–10 FPS for live enhancement and lane detection
  Demonstrated feasibility of real-time low-light processing

## Slide 16
Key Contributions
01
03
02
Developed an improved low-light image enhancement pipeline
Successfully deployed the system on PYNQ-Z2 hardware
Explored and compared multiple enhancement techniques
Designed an adaptive and stable enhancement approach
04
05
06
Integrated enhancement with lane detection system
Built a real-time processing pipeline

## Slide 17
01
03
02
04
Balancing high-quality enhancement with real-time performance was a major challenge, as improving visual quality often increased computational cost
some computationally intensive algorithms required simplification of pipeline to run efficiently on hardware with limited resources.
Preventing over-enhancement in extremely low-light scenerios required careful consideration of parameters and filtering methods
Ensuring stable and consistent lane detection across different lighting within the ROI was a difficult task and required for us to change ROI multiple times.
Challenges & Learnings
Understanding and optimizing trade-offs between accuracy, speed, and hardware constraints was critical for achieving real-time performance
05

## Slide 18
Future Work
  Implement FPGA-based acceleration to improve processing speed and achieve higher frame rates beyond current performance
  Explore deep learning-based approaches for more robust and accurate lane detection under complex real-world conditions
  Enhance performance under extreme lighting scenarios such as heavy glare, fog, and very low visibility environments
  Optimize the pipeline further for better resource utilization and improved efficiency on embedded hardware platforms
  Integrate the system into a complete ADAS(Advanced Driver Assistance Systems) framework for real-world deployment and testing

## Slide 19
Conclusion
  Developed an effective low-light image enhancement pipeline for improved visibility
  Enhanced lane detection performance under challenging low-light conditions
  Designed a simplified pipeline for real-time processing
  Successfully implemented and tested the system on PYNQ-Z2 hardware
  Demonstrated practical applicability for real-world driving scenarios

## Slide 20
Thank You
Questions Welcome